## Slide 1
COMPUTER NETWORKING & CYBER SECURITY
WESTFOLD
TEXTILE MILLS
Multi-Site Routing, Access Control & Address Translation
CASE STUDY NO. 46
Nishi Chopda
150096725128

## Slide 2
CASE STUDY & OBJECTIVES
Westfold Textile Mills consists of a Headquarters, a Weaving Plant, and the recently acquired Loomcraft Fabrics network. The network is designed to provide communication between these sites while maintaining the existing EIGRP environment at Loomcraft.
Case Study
KEY OBJECTIVES
  Multi-area OSPF for HQ–Plant routing
  EIGRP AS 950 for Loomcraft
  OSPF–EIGRP redistribution & summarization
  eBGP with two Internet Service Providers
  VLANs, ACLs & NAT/PAT for security and connectivity

## Slide 3
NETWORK TOPOLOGY & ADDRESSING
NETWORK SEGMENTS
  HQ–Plant: 172.31.0.0/30
  Plant LAN: 172.31.10.0/24
  Finance VLAN 15: 172.31.15.0/24
  Guest VLAN 85: 172.31.85.0/24
  Loomcraft: 172.31.50.0/24
  Public NAT Block: 198.51.100.24/29
7 Routers • 4 Switches • 10 End Devices • Dual ISP Connectivity

## Slide 4
ROUTING ARCHITECTURE
STATIC ROUTING
Initial Connectivity
  Initial HQ–Plant connectivity
  Default route from HQ-EDGE toward the ISP
  HQ–Plant static routes were later replaced by OSPF
OSPF adjacency: FULL • Plant route learned dynamically: 172.31.10.0/24
OSPF
Dynamic Routing
  Process ID: 10
  Area 0: HQ backbone
  Area 10: Plant LAN
  PLANT-ABR connects Area 0 ↔ Area 10
  DR/BDR election verified on Plant LAN

## Slide 5
EIGRP & REDISTRIBUTION
EIGRP — LOOMCRAFT
  AS 950
  Existing Loomcraft routing domain maintained
  Loomcraft LAN: 172.31.50.0/24
  PLANT-BOUNDARY acts as the routing boundary
ROUTE REDISTRIBUTION
  OSPF → EIGRP routes advertised to Loomcraft
  EIGRP → OSPF routes advertised toward HQ/Plant
  Bidirectional connectivity verified
ROUTE SUMMARIZATION
172.31.0.0/16
Internal Westfold networks summarized toward Loomcraft

## Slide 6
BGP ARCHITECTURE
  HQ-EDGE: AS 65120
  ISP-Crestline: AS 65022
  ISP-Harbor: AS 65023
  eBGP used between different Autonomous Systems
  Public network: 198.51.100.24/29
BGP & DUAL ISP CONNECTIVITY
Dual eBGP connections provide redundant Internet connectivity with failover between two independent ISPs.

## Slide 7
NAT/PAT & STATIC NAT
NAT / PAT
  Internal network: 172.31.0.0/16
  Public NAT block: 198.51.100.24/29
  PAT: 198.51.100.26 – .29
  HQ-EDGE performs NAT/PAT
  Multiple internal devices share public addresses through PAT
STATIC NAT
  Web Server: 172.31.10.21
  Public mapping: 198.51.100.30
  Fixed one-to-one mapping for external access
NAT/PAT and Static NAT were configured on HQ-EDGE for controlled Internet connectivity.

## Slide 8
NETWORK SECURITY
VLAN SEGMENTATION
  Finance VLAN: 172.31.15.0/24
  Guest VLAN: 172.31.85.0/24
  VLANs separate Finance and Guest traffic
  HQ-CORE subinterfaces provide inter-VLAN routing
ACCESS CONTROL LIST
  Extended ACL applied to Guest VLAN
  Guest → Finance traffic is denied
  Other required traffic remains permitted
ACL verification confirmed that Guest devices cannot initiate connections to the Finance VLAN.

## Slide 9
THANK YOU!
Westfold Textile Mills — Multi-Site Networking & Cyber Security